## Slide 1: EE476 Final Project Accumulator
Kendrick Tang, Sung Kim, and Cameron Forbis

## Slide 2: A Problem Statement
Build an accumulator that outputs sum of 64, 16 bit sign magnitude numbers in 22 bit twos complement format
Create built in self test unit using a 16 bit LFSR and 22 bit signal analyzer
Size design to drive 20fF load on outputs

## Slide 3: Approach
Use an adder and a partial sum register to accumulate a sum
Use a output register clocked every 64 cycles to store the output
Use a counter to clock the output register and reset the partial sums
Use muxes to switch between test IO and real IO.
Partial Sum Register
Output Register
+
LFSR
User Input
Counter

## Slide 4: A Design Flow
Identify components needed for the accumulator
Design components (adder, counter, FF, …)
Design top level integration
Perform simple tests on individual components
Perform a robust test on the accumulator
Layout
If time permits, optimize

## Slide 5: Adder Design
Carry look-ahead design
3 bit ripple-carry adders
Propagate, generate logic is formed with a single complex gate + nands/nors to get Pi_bar and Gi_bar

## Slide 6: A 22-bit adder

## Slide 7: A Ripple Counter

## Slide 8: Accumulator

## Slide 9: A Validation Method
Very simple tests for a few of the main components
  Full adder, 3-bit adder, 22-bit adder
  2’s-complement conversion
  64 stage counter
Simple test for accumulator
  Confirm basic behavior (e.g. output changes only every 64 cycles)
  Confirm simple accumulation of either positive or negative constant input
More robust accumulator test
  Determined input sequence generated by LFSR with MATLAB
  Determine result of signal analyzer after ()-cycles for small n
  Compare to schematic simulation

## Slide 10: An Update
What is done:
  Built simulators in MATLAB
  Confirmed schematic
  Layout complete of most simple cells
What is left:
  Finish the adder layout
  Finish layout of higher level components (registers, counters, LFSR, 22-bit adder, …)
  Wire the top level together
  If time permits, optimize
  Write report